## Slide 1: Brush Axes
http://www.americantrails.org/resources/info/tools3.html

## Slide 2: Brush Axe
A gardening and landscaping tool resembling an axe with a 12-inch (30 cm) curved blade and a 36-inch (91 cm) handle. It is commonly used by surveying crews to clear out heavy undergrowth from trails.
karlkuemmerling.com/store/product7.html

## Slide 3: Description and Use
In the construction industry the brush axe is very commonly used to clear brush when large mechanized equipment cannot maneuver in the area or where equipment will damage the area to be cleared.

## Slide 4: Description and Use
A brush axe is often used for the removal of brush that is too heavy for a weed eater and too light for an axe. It can be either double-edged or single-edged, but single-edged brush axes are most common. Swung like an axe with an overhead swing or swung horizontally, the brush axe's long 36 inch handle and heavy head give it a powerful cut.

## Slide 5: Vegetation Control
Brush Axes are a very effective tool for clearing the growth over hiking trails in hilly or mountainous regions where cumbersome equipment is impractical or impossible to use.
http://blueandwhitecrew.org/overseerinfo/vegetation.php

## Slide 6: Safety Guidelines
Safety Concerns
  Defective Tool
  Insufficient PPE
  Improper technique
  Uncontrolled surroundings
The major problem with the brush axe is that its ability to injure is not respected and it is not taken seriously.
http://www.tpub.com/content/shopequipment/TM-9-243/css/TM-9-243_253.htm

## Slide 7: Safety Guidelines
Handles with splinters, cracks, excessive twist or warp should be replaced or reconditioned.
The axe head must be kept sharp and free of burrs and nicks
The axe head must be set firmly on the handle
When storing the axe, coat lightly with oil

## Slide 8: Injuries: Brush Axe
Lacerations
Sprains and Strains
Blunt force trauma
Blisters
Eye Injuries
Others: Chiggers, Ticks, Snakes, Poison Ivy
http://www.aurorahealthcare.org/yourhealth/healthgate/getcontent.asp?URLhealthgate=%22101013.html%22

## Slide 9: Fatalities
There have been no recorded fatalities directly linked to the use of the Brush Axe according to the OSHA fatality data from 1990 to 2009.

## Slide 10: OSHA Regulations
There is no specific reference in the OSHA regulations regarding the Brush Axe. The following are generic regulations that should be followed when using any hand tool of this nature.

## Slide 11: OSHA Regulations
1910.266(e)(1)(i)The employer shall assure that each hand and portable powered tool, including any tool provided by an employee, is maintained in serviceable condition.
1910.266(e)(1)(ii)The employer shall assure that each tool, including any tool provided by an employee, is inspected before initial use during each work shift. At a minimum, the inspection shall include the following:
1910.266(e)(1)(ii)(A)Handles and guards, to assure that they are sound, tight-fitting, properly shaped, free of splinters and sharp edges, and in place
http://www.osha.gov/SLTC/etools/logging/sections/preamble/tools_preamble.html

## Slide 12: PPE
Long Pants
Long-sleeved Shirt
Goggles
Gloves
Hard Hat
Steel Toe Boots
http://www.tpub.com/content/construction/14256/img/14256_281_3.jpg

## Slide 13: Technique
Be sure to stand clear of others (6-8 ft)
Check swing clearance (hanging limbs and vines)
Watch for residual stubble on ground
Maintain good posture, feet apart
Take measures against bugs, snakes, and harmful plants through PPE and clothing
Maintain a firm grip on handle
Cut with a slicing rather than a hacking motion and pull back on tool at the end of the swing to utilize the curved blade
Carry tool with the head forward like a shovel when transporting

## Slide 14: Best Practices
Workers Should:
  Inspect the area to be cleared for hanging limbs and branches that could compromise proper swing technique
  Inspect the tool; head, handle, attachment
  Take frequent breaks; hydrate
http://www.tpub.com/content/construction/14256/css/14256_281.htm

## Slide 15
Think Safety
Work Safely