## Slide 1: Impact Wrench Safety

## Slide 2: Impact Wrenches
A socket wrench power tool used to tighten nuts and bolts.
Designed to deliver high torque output by storing energy in a rotating mass, then delivering it suddenly to the output shaft.

## Slide 3: Power Sources for Impact Wrenches
Compressed Air
  (most common)
Electric
Hydraulic
Portable/Battery Powered

## Slide 4: Types of Impact Wrenches
Impact wrenches are made in a variety of shapes and sizes
Shapes
  Inline
  Butterfly
  Pistol Grip
Socket Drive Sizes
  From ¼” to over 3 ½”

## Slide 5: Industry Uses
Construction
Automotive
Heavy Equipment Maintenance
Product Assembly

## Slide 6: Industry Uses
When used in construction, the primary use is in steel erection
  Extremely high torque is needed to tighten nuts and bolts to connect steel members

## Slide 7: Typical Hazards
Rupturing of oil or air lines used to power tool
  Oil under pressure easily punctures the skin, causing serious injury, gangrene or death.
  Flying oil or debris can easily damage eyes.
Routing of pneumatic or hydraulic hoses or power extension cords to create trip hazards
Sudden torque forces generated by the impact wrench can cause a worker to lose balance or to receive a wrist injury
Damaged hoses or extension cords
Source: http://65.36.183.19/greenlee/im/99924641rev05.pdf

## Slide 8: Typical Hazards
Dropping the impact wrench from elevation
Heat
  Impact wrench generates heat
  Contact with hot surface of impact wrench can easily burn user.
Moving Parts
  Fingers and clothing can get caught
Noise
Source: http://65.36.183.19/greenlee/im/99924641rev05.pdf

## Slide 9: There Was One Worker Fatality Investigated By OSHA Between 1990-2009
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 10: Fatality Example
A worker was walking on a 1:12 pitch roof. He slid an impact wrench down to the edge on a 90 foot wide roof.
He misjudged the roof condition (light frost on roof) and the impact wrench continued to slide down the roof. Fearing that it would go over the roof edge the worker began running after the wrench.
The worker dove to stop it, but slid off the roof edge on his stomach and fell 23 feet on the asphalt driveway. He died from his injuries.
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 11: OSHA Regulations
There are no OSHA regulations pertaining specifically to impact wrenches.
Source: Information extracted from OSHA Regulations (Standards - 29 CFR)

## Slide 12: Safe Work Practices
Personal Protective Equipment
  Gloves
  Slip Resistant Footwear
  Eye Protection
  Close Fitted Clothing
  Hearing Protection
  Head Protection

## Slide 13: Safe Work Practices
Keep work area clean
Use the proper tools for the job
  i.e. – there are sockets designed specifically for use with impact wrenches
Maintenance
  Service and maintenance should be performed regularly by qualified technician to ensure safety and performance.
Check for damaged parts
Tie tool off when working at elevations

## Slide 14: Safe Work Practices
Remove adjusting keys and wrenches that were used to make adjustments on the impact wrench
Avoid unintentional starting
  Be sure switch is in the OFF position when not in use and before attaching power source.
Disconnect from power source when not in use
Store idle equipment in dry location to prevent rust
Route hoses in a safe manner
  Prevent entanglement and tripping caused by hoses
  Check hoses/cords for damage, remove from service if damaged

## Slide 15: Think Safety Work Safely