## Slide 1: Pruning Saws
http://2.bp.blogspot.com/_kM7t6IwmQlQ/SQc65HgEWBI/AAAAAAAAE4Y/8CHm5hW_L4g/s400/professional+pruning+saws.JPG
Notes: First Slide

## Slide 2: Description
Pruning saws allow for quick and easy cutting of smaller branches and limbs. They are especially useful when cutting sticky, gummy plants and live wood. Pruning saws come in fixed and folding blade designs, and some have belt scabbards so they are always handy.
http://gardening.about.com/od/toolschool/ig/Pruning-Tools/Pruning-Saws.htm
http://ecx.images-amazon.com/images/I/31Zdk9SnemL._SL500_AA300_.jpg
An example of a pruning saw.
Notes: Description / Historical Data

## Slide 3: Kinds of Pruning Saws
Curved Blade Saw
Best for home use and in nurseries
This type has a 12” -16” blade with six teeth per inch
http://ecx.images-amazon.com/images/I/31Zdk9SnemL._SL500_AA300_.jpg
An example of a curved blade pruning saw.

## Slide 4: Kinds of Pruning Saws
Straight Double-Edged Saw
Best for cutting sap or green wood
This type has a 6 - 8 teeth per inch on one side and 4 - 6 larger teeth per inch on the other side
An example of a straight double-edged pruning saw.
http://www.fhwa.dot.gov/environment/Fspubs/05232810/fig023.gif

## Slide 5: Kinds of Pruning Saws
Tri-Cut Blade Saw
This type has teeth that are sharpened on three sides, like a triangle
Designed to cut faster and easier
Stays sharper longer than traditional saws
An example of a tri-cut blade.
http://esscodist.com/shopsite_sc/store/html/media/Trie250.GIF

## Slide 6: Kinds of Pruning Saws
Tree Saws
  This type has a straight or curved 12- 16 inch blade and a pistol style handle
  The saw’s teeth cut on the pull stroke and slides back on the push stroke
An example of a tree pruning saw.
http://www.fs.fed.us/eng/pubs/htmlpubs/htm88232601/images/proprune.jpg

## Slide 7: Kinds of Pruning Saws
Folding Saws
Ideal for light pruning
Very portable and safe to transport
http://www.heimerdingercutlery.com/pruning-tools-felco-pruning-saws-c-29_78.html
An example of a folding pruning saw.

## Slide 8: Kinds of Pruning Saws
Pole and Rope Saws
Used for cutting high limbs without the aid of a cherry-picker
However, found to be difficult and awkward to use
An example of a pole and rope pruning saw.
http://www.benmeadows.com/images/xl/CORONA-Professional-Pole-Saw-BEN-_i_bmw150430.jpg

## Slide 9: Construction Uses
Pruning saws have a blade that is used to cut branches and small trees. Their construction use relates primarily to landscaping and site clearing. Pruning saws can be used for thick or high, difficult to reach branches.
A worker using a pruning saw for site clearing.
http://www.fs.fed.us/eng/pubs/htmlpubs/htm88232601/images/figure04.jpg
Notes: Relevance to Construction

## Slide 10: Pruning Hazards
Many pruning activities require workers to enter into thick brush, creating a safety hazard. Such an environment can cause skin lacerations or eyes harmed due to ricocheting branches, flying debris, or sharp twigs.
A potentially hazardous area in which pruning saws would typically be used.
http://www.pansite.org/vegetation.JPG

## Slide 11: Pruning Hazards
Sawing branches may cause particulate matter to fill the air. This presents an inhalation hazard.
Falling limbs and debris are dangerous and may be fatal.
Branches or Foliage
http://static.howstuffworks.com/gif/rd/how-to-know-when-to-use-saws-for-pruning-trees0.jpg
Cutting branches with pruning saws can be hazardous.

## Slide 12: Pruning Hazards
It is important to check the condition of the pruning blade before use. A dull or rusty blade can be a safety hazard as well as inefficient.
Blade Condition and Maintenance
http://www.ehow.com/pruning-saw/#ixzz1HSJ6f3AQ
http://i.ehow.co.uk/images/a07/a8/ca/remove-rust-saw-800X800.jpg
Pruning saws need regular maintenance and upkeep to keep them in pristine condition.
Notes: Typical hazards / Safety concerns

## Slide 13: Pruning Hazards
Pinch Point: Many pruning saws are collapsible. Fingers could be caught between the blade and the handle
Slipping: Proper control must be maintained over the blade to avoid slipping. A slip could result in a severe cut.
Breaking: Using excessive force while pruning may cause the blade to break. The resulting metal shards could injure the user
Pruning Saws

## Slide 14: Pruning Hazards
Bees, wasps, snakes and ticks within trees and foliage.
Heat stroke
Poison Ivy
Miscellaneous
http://thepracticalhorse.com/_Media/poison_ivy.jpg
kauaihoney.com/images/FeralHive.jpg
Bee hives can hang from branches that need to be pruned, causing greater potential for stings.
Workers can brush up against poison ivy while pruning, causing skin irritation.

## Slide 15: Pruning Hazards
Often times pruning activities take place in high trees which leads to falling concerns. The fact that a pruning saw is involved may cause a hazard in itself. For instance, a falling worker may land on an open pruning saw they were working with.
Fall Potential

## Slide 16: Example of Pruning Fatalities
A worker died while pruning trees in Scotland when he plunged 30ft from a cherry picker.
Worker pruning on a cherry picker.
http://www.friendsofthekoala.org/fok/files/images/koala%20country%20energy%20cherry%20picker%20003.preview.jpg
www.dailyrecord.co.uk/.../man-dies-after-falling-from-cherry-picker-as-he-pruned-trees-86908-21441916/
Notes: Statistics of fatalities

## Slide 17: Example of Pruning Fatalities
A worker was trimming trees along an electric utility line. Numerous high- and low-voltage lines ran through the trees at various heights in this area. The worker was trimming a large branch when he leaned back to prune some small branches above his head. The back of the victim's neck came into contact with a 7,200-volt power line and he was electrocuted.

## Slide 18: OSHA and Pruning Saws
OSHA has not recorded any serious injuries or deaths related to pruning saws from 1990 thru 2009.
http://www.commercialcleaningincharlotte.com/wp-content/uploads/2009/05/osha-logosvg.png
An image of the OSHA logo.
Notes: OSHA regulations

## Slide 19: OSHA and Pruning Saws
There are no OSHA regulations directly pertaining to pruning saws.
http://eshpartnering.com/topics/wp-content/uploads/2010/04/OSHA-poster.jpg
An example of a OSHA poster.

## Slide 20: Pruning Safety
Pruners should wear protective eyewear, gloves, headwear, shoes, long-sleeved shirts, and pants
Wear light-colored, thin clothing for hot days and warmer layers for cold or wet days.
Wear sunscreen and wide-brimmed hats to protect against the sun
Proper Attire
Examples of proper protective equipment.
http://www.cordless-drills.net/images/pictures/ao-safety-sx-safety-eyewear-full-frame-clear-lens.jpg
http://thatwoman.files.wordpress.com/2008/07/hard_hat.jpg

## Slide 21: Pruning Safety
Before pruning begins, survey the area for hidden hazards such as snakes, bees, and poison ivy. Workers should be trained in pruning hazards, safe pruning techniques, proper tool handling, ladder safety, and appropriate personal protective equipment.
Proper Training
Notes: Safety Procedures / Best Practices

## Slide 22: Pruning Safety
Never prune trees or branches within 10 feet of power lines.
Maintain a safe working distance from other people when using pruning tools.
Do not attempt to cut branches bigger than the pruning tool was designed to cut.
Proper Practices
Should not prune trees or branches within 10 feet of a power line.
http://www.srpnet.com/electric/graphics/pruning2.gif
Notes: Tied off?

## Slide 23: Pruning Safety
Maintain a constant awaremess of the location of hands and fingers.
The blade on a pruning saw needs to be sharpened with regular sharpening tools.
Sheath pruning saws immediately after use to prevent accidental cuts.
Proper Practices
http://www.yates.co.nz/images/nz/products/books-tools-and-propagation/ars-pruning-saw-and-sheath-cam-24ln.jpg
Covering pruning saws when not in use is safe practice.

## Slide 24
Think Safety
Work Safely
Notes: Last Slide