## Slide 1: Reciprocating Saws
http://www.milwaukeetool.com/CMS/Publications/Super%20Sawzall%206538-21_FR.jpg

## Slide 2: Introduction
A reciprocating saw is a type of saw in which the cutting action is achieved through a back and forth motion of a toothed blade
Typically used in the construction industry for demolition and rough cutting of drywall, metal, plaster, tubing, and wood
Commonly referred to as a Sawzall
http://en.wikipedia.org/wiki/Reciprocating_saw

## Slide 3: Features and Controls
http://www.milwaukeetool.com/CMS/Diagrams/58-14-4126d2.pdf
Handle with Variable Speed Trigger
Motor
Insulating Boot
Blade Clamp
Front Handhold
Saw Blade
Adjustable Pivot Shoe

## Slide 4: Operation
http://www.milwaukeetool.com/CMS/Diagrams/58-14-4126d2.pdf
For cutting from an edge, align the blade with the cutting surface before pulling the trigger
Always hold the shoe flat against the work piece to avoid excess vibration

## Slide 5: Operation
http://www.extremehowto.com/xh/hotprod_images/4_2005_0414alligator0017.jpg
For plunge cuts, rest the shoe on the work surface and with the blade about to contact the material, pull the trigger
As the blade begins cutting, raise the handle of the saw until the shoe firmly contacts the cutting surface

## Slide 6: Injuries
Most injuries occur to the fingers, hands, and arms in the form of lacerations and amputations due to improperly handling the saw and not following safety guidelines
Other reported injuries have occurred due to electrocution and collapsing loads
http://www.associatedcontent.com/article/2536917/common_saw_defects_and_sawrelated_injuries.html

## Slide 7: OSHA Statistics
Chart: 
| Struck by Blade | Crushed by Debris | Heart Failure | Struck by Debris | Electrical Shock
 | 1 | 1 | 1 | 2 | 5
There were 10 fatalities involving reciprocating saws that were investigated by OSHA from 1990 thru 2009
Source: Extracted from OSHA Accident Investigation Data 1990-2009
Electrical Shock
50%
Struck by Blade
10%
Crushed by Debris
10%
Struck by Debris
20%
Heart Failure
10%

## Slide 8: Fatalities
A worker was demolishing an interior partition using a portable reciprocating saw when he was struck by debris from the partition, causing him to fall from a ladder. He died from his injuries.
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 9: Fatalities
A worker was cutting a ceiling joist when he hit a section of Romex electrical wire. He continued to saw which resulted in his electrocution.
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 10: Fatalities
A plumber was attempting to cut a hole in a roof when he lost control of the Sawzall and struck himself between his eye and temple with the blade. The plumber later died from his injuries.
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 11: OSHA Regulations
1926.300(d)(2)
  Reciprocating saws…with blade shanks greater than a nominal one-fourth inch…shall be equipped with a constant pressure switch or control, and may have a lock-on control provided that turnoff can be accomplished by a single motion of the same finger or fingers that turn it on.
http://www.osha.gov/pls/oshaweb/owadisp.show_document?p_table=STANDARDS&p_id=10688

## Slide 12: Personal Protective Equipment
Leather or general work gloves
  To ensure proper grip on saw
  To protect hands from saw blade and debris
Safety glasses
  To protect eyes from debris or broken blade
http://guttercleaningtips.com/work-gloves/

## Slide 13: Safety Procedures
Read Operating Instructions Before Use
Avoid accidental starting by ensuring switch is off prior to plugging into outlet
Check blade for breakage before each use
http://www.milwaukeetool.com/CMS/Diagrams/58-14-4126d2.pdf

## Slide 14: Safety Procedures
Discontinue use if power switch is malfunctioning
Remove blade tightening key or wrench before turning power on
Use clamps or other restraining devices to secure and support work piece to stable platform
http://www.milwaukeetool.com/CMS/Diagrams/58-14-4126d2.pdf

## Slide 15: Safety Procedures
Keep cutting edges sharp and clean
Keep hands away from all cutting edges and moving parts
When possible, keep the shoe flat against the material being cut
Wear insulating gloves when cutting operations are performed where the blade may contact hidden wiring
http://www.milwaukeetool.com/CMS/Diagrams/58-14-4126d2.pdf

## Slide 16: Safety Procedures
Do not handle by the cord at any time
Do not force through cutting material
Do not overreach but keep proper footing and balance
Disconnect from power before making any adjustments, changing accessories, or storing
http://www.milwaukeetool.com/CMS/Diagrams/58-14-4126d2.pdf

## Slide 17: Think Safety
Work Safely