## Slide 1
Scrapers
Caterpillar 613C Scraper

## Slide 2
Scrapers are a type of heavy machinery used for earthmoving
Scrapers are capable of excavating, hauling, and dumping material over medium-to long haul distances.
Scrapers are useful construction equipment when hauling distances range between 500 to 3000 feet.
Source: Caterpillar Performance Handbook: Edition 24, 8-1 to 8-5
S. W. Nunnally, Construction methods and management, 7th edition, 2007
What is scraper?

## Slide 3
Loading and transporting earth over short and medium distances.
Source: www.terex.com/main.php?obj=prod&action=VIEW&id=21&nav=prod&cid=e3959eefdc65adcc4e0e616b833694b1
Standard usage

## Slide 4
Self-propelled scrapers were invented in the 1930s by R.G. LeTourneau
Source: Dr. John H. Niemela, “A History of R.G. LeTourneau’s Earliest Scrapers,” Ver. 1.1B 10–31–07, MoL©
History of scraper

## Slide 5
Source: United States Army Training Support Center
Components of scraper

## Slide 6
The scraper excavates (cuts) by lowering the front edge of its bowl into the soil. The bowl front if equipped with replaceable blades, which may be straight, curved, or extended at the center.
Source: S. W. Nunnally, Construction methods and management, 7th edition, 2007
How it works?

## Slide 7
Hopper (the rear part of the machine ) is lowered or raised to cut into the ground collecting the dirt
The collected earth can be moved and dumped accordingly as this process is repeated
Some scrapers work in tandem with a bulldozer
Source: S. W. Nunnally, Construction methods and management, 7th edition, 2007
How it works?

## Slide 8
Features of Caterpillar Scrapers include:
Standard cubic yard capacities range from 14 yd3 to 66 yd3
Weight of machinery can be 67,195 lb up to 146,770 lb
Source: Caterpillar Performance Handbook: Edition 24, 8-1 to 8-5
Some features

## Slide 9
Each type has different characteristics of rolling resistance, maneuverability, stability, and speed in operation.
Although there are a number of different types of scrapers, principal types are as follows:
types of scrapers

## Slide 10
Single engine overhung (two or three axle) scrapers
Major types of scrapers

## Slide 11
Twin-engine all-wheel-drive scrapers
Cat 627 Twin Engined Scraper
Major types of scrapers

## Slide 12
Towed scrapers
Major types of scrapers

## Slide 13
Towed Scrapers
Capacity (heaped) - 18.8 yd3 to 23.5 yd3
Capacity (struck) - 13 yd3 to 17 yd3
Least expensive
Source: http://www.cat.com/cda/layout?m=111776&x=7

## Slide 14
Elevating scrapers
(also known as Paddle Wheel or Self-loading scrapers)
Caterpillar 615C elevating scraper
Caterpillar 633 elevating scraper
Caterpillar 633D elevating scraper
Michigan scraper
Major types of scrapers

## Slide 15
Elevating Scrapers
Capacity(heaped) - 11 yd3 to 23 yd3
Max. Speed - 24.4 mph to 32 mph
Ability to homogenize
and condition soil
while loading
Source: http://www.cat.com/cda/layout?m=111776&x=7

## Slide 16
Auger Scrapers
Caterpillar 627G Auger Scraper
Major types of scrapers

## Slide 17
Push-pull (twin-hitch) scrapers
Caterpillar 637E tandem push-pull scraper
657G Push Pull Scraper
Major types of scrapers

## Slide 20
Open-bowl scrapers
(Capable of being loaded by front-end loaders or hydraulic excavators)
Caterpillar 621 open bowl scraper
Caterpillar 627F tandem open bowl scraper
Caterpillar 631E open bowl scraper
Caterpillar 651 open bowl scraper
Major types of scrapers

## Slide 21
Open Bowl Scrapers
Capacity (heaped) - 22 yd3 to 44 yd3
Max. Speed - 32 mph to 36 mph
Often have push/pull
ability
Source: http://www.cat.com/cda/layout?m=111776&x=7

## Slide 22
Coal Bowl Scrapers
Capacity (heaped) - 50 yd3 to 73 yd3
Max. speed - 31.1 mph to 34.1 mph
Often powered by
twin engines
Most Expensive
Source: http://www.cat.com/cda/layout?m=111776&x=7

## Slide 23
Rolling over on uneven ground and during turns, especially with full loads
Failure of brakes or other machinery components
Low visibility behind and around the machine
Crushing and wedging in between other objects
Scraper hazards

## Slide 24
Failure of safety measures such as ROPS, backup alarms, safety belts
Poor communication among workers and operators
Hazardous road conditions
Dangerous maintenance situations
Some concerns

## Slide 25: Scraper Fatality Statistics From 1990 thru 2009 OSHA investigated 52 incidents involving scrapers
Chart: 
| Run Over | Explosion | Crushed | Struck by | Fall | Drowning
Column1 | 20 | 3 | 14 | 10 | 4 | 1

## Slide 26: Type of Scraper Movement
Chart: 
| Forward | Reverse | Stationary
Column1 | 21 | 18 | 13

## Slide 27
An operator was pulling a pan scraper with a tractor
The operator was driving along a ditch
The slope caused a rollover
The man was crushed because of a lack of rollover protection
Source: Extracted from OSHA Accident Investigation Data 1990-2009
Fatality Example 1

## Slide 28
Operator was working with a surveyor
The surveyor knelt down to place a grade stick
The backup alarm was not working and the operator backed over the surveyor with a scraper
There was no third observer to communicate between the two men
Source: Extracted from OSHA Accident Investigation Data 1990-2009
Fatality Example 2

## Slide 29
An employee just finished dumping a full pan load
As he made another pass he fell off of the machine
He was run over by the front left tire
Source: Extracted from OSHA Accident Investigation Data 1990-2009
Fatality Example 3

## Slide 30
The owner/operator of an E200 International was completing a sharp left turn down a slope
The right rear wheel lifted off the ground and the scraper tilted down the hill
The machine rolled over and crushed the operator
Source: Extracted from OSHA Accident Investigation Data 1990-2009
Fatality Example 4

## Slide 31
An employee was standing next to a scraper with his back facing another scraper
To move out of the way, the operator shifted the front scraper in reverse
The employee on the ground was crushed between the two machines
Source: Extracted from OSHA Accident Investigation Data 1990-2009
Fatality Example 5

## Slide 32
A scraper was parked on a downhill incline
The scraper rolled forward and pinned an employee between the scraper and a service truck.
Source: Extracted from OSHA Accident Investigation Data 2007-2009
Fatality Example 6

## Slide 33
A worker noticed a piece of wood lodged in the cables under the scraper
He told the operator to wait a minute but the message was missed due to the operator talking on his mobile telephone
The employee was crushed by the rear tire when the operator proceeded to drive the scraper
Source: Extracted from OSHA Accident Investigation Data 2007-2009
Fatality Example 7

## Slide 34
Subpart O- Motor Vehicles, Mechanized Equipment, and Marine Operations
  1926.602 Material Handling Equipment
    9. Audible alarms.
      (I) All bidirectional machines, such as {…} [scrapers] shall be equipped with a horn, distinguishable from the surrounding noise level, which shall be operated as needed when the machine is moving in either direction. The horn shall be maintained in an operative condition.
Source: OSHA 29 CFR 1926 Construction Industry Regulations
OSHA regulations

## Slide 35
Subpart W:
  1926.1000(c)(2) Rollover protective structures (ROPS) and supporting attachment shall [be] {…} installed in a manner which will support, based on the ultimate strength of the metal, at least two times the weight of the prime mover applied at the point of impact.
Source: OSHA 29 CFR 1926 Construction Industry Regulations
OSHA regulations

## Slide 36
1926.1000(c)(2)(i) The design objective shall be to minimize the likelihood of a complete overturn and thereby minimize the possibility of the operator being crushed as a result of a rollover or upset.
Source: OSHA 29 CFR 1926 Construction Industry Regulations
OSHA regulations

## Slide 37
1926.600(a)(3)(i) scraper blades {…} shall be either fully lowered or blocked when being repaired or when not in use. All controls shall be in a neutral position, with the motors stopped and brakes set, unless work being performed requires otherwise.
Source: OSHA 29 CFR 1926 Construction Industry Regulations
OSHA regulations

## Slide 38
1926.602(a)(2)(i) Seat belts shall be provided on all [scrapers]. and shall meet the requirements of the Society of Automotive Engineers, J386-1969, Seat Belts for Construction Equipment.
Source: OSHA 29 CFR 1926 Construction Industry Regulations
OSHA regulations

## Slide 39
1926.602(a)(4) All earthmoving equipment [including scrapers] shall have a service braking system capable of stopping and holding the equipment fully loaded, as specified in Society of Automotive Engineers SAE-J237.
Brake systems for self-propelled rubber-tired off-highway equipment manufactured after January 1, 1972 shall meet the applicable minimum performance criteria set forth in the following Society of Automotive Engineers Recommended Practices:
Self-Propelled Scrapers; SAE J319b-1971.
Source: OSHA 29 CFR 1926 Construction Industry Regulations
OSHA regulations

## Slide 40
1926.602(a)(5) Pneumatic-tired earth-moving haulage equipment [ such as scrapers] whose maximum speed exceeds 15 miles per hour, shall be equipped with fenders on all wheels to meet the requirements of Society of Automotive Engineers SAE J321a-1970, Fenders for Pneumatic-Tired Earthmoving Haulage Equipment.
An employer may, of course, at any time seek to show under 1926.2, that the uncovered wheels present no hazard to personnel from flying materials.
Source: OSHA 29 CFR 1926 Construction Industry Regulations
OSHA regulations

## Slide 41
1926.1000(c)(2)(ii) The design shall provide a vertical clearance of at least 52 inches from the work deck to the ROPS at the point of ingress or egress.
1926.1000(d) Remounting. ROPS removed for any reason, shall be remounted with equal quality, or better, bolts or welding as required for the original mounting.
1926.1000(e) Labeling. Each ROPS shall have the following information permanently affixed to the structure:
Manufacturer or fabricator's name and address;
ROPS model number, if any;
Machine make, model, or series number that the structure is designed to fit.
Source: OSHA 29 CFR 1926 Construction Industry Regulations
OSHA regulations

## Slide 42
Proper operation and maintenance of the scraper prevents accidents !

## Slide 43
DRESS RIGHT FOR THE JOB:
Safety hat
Safety Shoes
Safety Glasses / Goggles
Heavy Gloves
Hearing Protection
Reflective Vest
Respirator(when needed)
Source: Construction Industry Manufacturers Association, Scraper safety manual for operating and maintenance personnel, 1980
Safe work practices - PPE

## Slide 44
Think ahead! Become familiar with all conditions in the area, such as:
  Condition of haul roads.
  Holes, obstructions, mud and ice.
  Traffic routes and rules.
  Dust, smoke or fog.
  Underground utilities
Know the working area
Source: Construction Industry Manufacturers Association, Scraper safety manual for operating and maintenance personnel, 1980

## Slide 45
Read the manufacturer’s operating manual.
Know the capabilities of the equipment; and its limitations.
Become thoroughly familiar with all controls, gauges and instruments.
Work slowly and carefully
until accustomed with the equipment.
Know the protective devices on the scraper. For example: Guards, Canopies / Roll-over Protective Structures, Shields, Backup Alarms, Seat Belts.
Pre-operation instructions
Source: Construction Industry Manufacturers Association, Scraper safety manual for operating and maintenance personnel, 1980

## Slide 46
Walk-Around the scraper at the start of each shift; and inspect:
Check to be sure there is nobody working on it, under or nearby.
Check the area to be sure it is clear of obstructions and/ or people.
Machine and engine compartments / instruments
Check utility / pressurized lines
Safety devices
Pre-operation walk-around check
Source: Construction Industry Manufacturers Association, Scraper safety manual for operating and maintenance personnel, 1980

## Slide 47
Brake systems
Headlights and warnings
Dirt or trash buildup
Oil or coolant leaks
Structural maladjustments/ Looseness/ cracks
Wear or damage to moving parts
The scraper operator is responsible for operations and has the authority to stop work when conditions are unsafe.
Pre-operation walk-around check
continued
Source: Construction Industry Manufacturers Association, Scraper safety manual for operating and maintenance personnel, 1980

## Slide 48
Sound horn before starting
Observe all signs and signals
Mount and dismount carefully (Never forget three-point contact!)
Check warning devices
Obey traffic rules
Maintain control of scraper at all times
Be sure that communication between ground employees is clear and evident
Safe work practices - DOs

## Slide 49
Don’t overspeed especially with full pans
Don’t carry passengers
Don’t service a machine in motion
Don’t operate an unsafe machine
Don’t engage in horseplay
Don’t forget safety belt. Uneven terrains may cause a scraper to tilt
Safe work practices – DON’Ts

## Slide 50
Be aware of overhangs / electrical wires, slide areas, or other dangerous conditions
Cross ditches, sidehills and ridges slowly, usually at an angle
Do not coast in neutral
Make sure clearance flags and other required warnings are on machine when roading
Watch for flagman or other personnel
Always apply retarder / brakes to reduce speed before entering sharp turns
Always anticipate grade; and select proper gearing range accordingly.
Operating scraper - safely
Source: Construction Industry Manufacturers Association, Scraper safety manual for operating and maintenance personnel, 1980

## Slide 51
Attach appropriate warning tags to the steering wheel to prevent accidents.
Read and understand maintenance, lubrications, and engine manuals.
Keep hands and clothing away from moving parts.
Lower all raised equipment before servicing. Always block the apron and ejector securely.
Do not use gasoline or diesel fuel to clean parts.
Pressurized systems / Electrical systems can cause burns or serious injuries if not handled properly.
Service and repair scraper - safely
Source: Construction Industry Manufacturers Association, Scraper safety manual for operating and maintenance personnel, 1980

## Slide 52
Think safety
Work safely