## Slide 1: Wheelbarrow Safety
http://www.google.com/images

## Slide 2: Definition
A wheelbarrow is a small hand-propelled vehicle, usually with just one wheel (some have two wheels), designed to be pushed and guided by a single person using two handles to the rear.
Source: http://en.wikipedia.org/wiki/Wheelbarrow
http://www.google.com/images

## Slide 3: Design Concept
Wheelbarrows are designed to distribute the weight of the load between the wheel and the operator, enabling the convenient carriage of heavier and bulkier loads than would be possible if the weight was carried entirely by the operator
http://www.google.com/images
Source: http://en.wikipedia.org/wiki/Wheelbarrow

## Slide 4: History
The wheelbarrow may have been invented in Ancient Greece in the early 400’s B.C.
  It was primarily used on construction sites
It reappeared in Medieval Europe sometime between 1170 and 1250
  It was used for building construction, mining operations, and agriculture
Source: http://en.wikipedia.org/wiki/Wheelbarrow

## Slide 5: History
China also had a version of the wheelbarrow. The first descriptions came from the 2nd century Han Dynasty tomb murals and brick tomb reliefs
  It was used for transporting military supplies
Source: http://en.wikipedia.org/wiki/Wheelbarrow

## Slide 6: History
  The Chinese wheelbarrow had a wheel in the center of the barrow whereas the European wheelbarrow had a front-mounted wheel similar to modern wheelbarrows
http://www.google.com/images
Source: http://en.wikipedia.org/wiki/Wheelbarrow

## Slide 7: Design Over Time
The wheelbarrow has evolved from using rocks as wheels, to wood as wheels, to modern designs in which rubber tires are used
Some wheelbarrows are equipped with two wheels to allow for greater support
http://www.google.com/images
Source: http://en.wikipedia.org/wiki/Wheelbarrow

## Slide 8: Safety Concerns
Tip-overs
Falls
Blisters
Splinters
http://www.google.com/images

## Slide 9: Potential Hazards
Unguarded edges
Narrow walkways
Uneven ground
Obstacles
Inclines
http://www.google.com/images

## Slide 10: Statistics on Fatalities
Most wheelbarrow fatalities are due to falls or struck-by accidents
The falls occurred primarily on roofing jobs where wheelbarrows were used with inappropriate guardrail systems or unguarded openings
The struck by accidents were caused by loss of control of another piece of equipment that subsequently killed the worker operating a wheelbarrow
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 11: Fatality Statistics (11 Cases)
Chart: 
| Struck-by | Falls
Falls vs. Struck-by Accidents | 3 | 10
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 12: Case #1
A worker was using a wheelbarrow to dump debris from a reroofing job into a trash chute that was hung from a parapet wall. The chute was accessed by a ramp which led to the top of the parapet wall and the chute opening.
There was a 2 inch square bumper at the end of the ramp (smaller than required by OSHA - 4 inches thick and 6 inches high) and there was no guardrail across the chute opening. While dumping a load of debris the worker was killed when he fell into the chute, landing 50 feet below in a dumpster.
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 13: Case #2
Three workers were removing roofing on a 5:12 pitch roof that had a 3 ft flat surface around the perimeter. One worker had loaded a wheelbarrow with roofing debris and was walking backward with the wheelbarrow along the 3 ft flat roof perimeter.
He either tripped, lost his balance, or lost his perspective of where he was. He fell from the roof's edge and was killed by the 30-foot fall. The roof had no catch platform nor were the workers using safety belts with lifelines.
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 14: Case #3
A worker was removing the bricks from a low sloped metal roof with a wheelbarrow. She had made a few trips to the leading edge to dump bricks over the side. The wheelbarrow path led past an unguarded skylight.
After dumping the bricks over the side, the worker turned around, grabbed the wheelbarrow with her arms behind her back and proceeded up the roof to the work area. While pulling the wheelbarrow up the roof, she stepped through an unguarded skylight and fell 23 feet to her death.
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 15: Case #4
A worker was delivering concrete mortar with a wheelbarrow to a wooden platform, which was covering a stairwell shaft opening. The wooden platform gave way and the employee fell 32 feet to his death.
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 16: Case #5
A concrete truck was making a delivery. The driver observed a worker lift the wheelbarrow handles and take two steps toward a nearby testing area. The driver put the truck in reverse and began to back toward the pour location.
Apparently, the laborer had difficulty balancing and moving the full wheelbarrow. The truck had backed up about15 ft when he ran over the worker who died immediately.
Source: Extracted from OSHA Accident Investigation Data 1990-2009

## Slide 17: OSHA Regulations
OSHA Standard - 1926.852(f)
  Where the material is dumped from mechanical equipment or wheelbarrows, a securely attached toe board or bumper, not less than 4 inches thick and 6 inches high, shall be provided at each chute opening
http://www.google.com/images

## Slide 18: Personal Protective Equipment
Main
  Heavy-duty gloves
  Steel-toe boots
Additional
  Hard Hat
  Cover-all clothing
  Safety glasses
  Safety vest
  Back brace
http://www.google.com/images

## Slide 19: Best Practices
Damage
  Check for damage to the frame and bucket
  Make sure the tires are fully inflated
Loading
  Do not overfill the wheelbarrow
  Keep items from sticking out over the sides of the bucket
  Take into account the weight to strength ratio of the wheelbarrow to the worker
  Make sure that it is loaded evenly
http://www.google.com/images
Source: http://www.ehow.com/about_6396476_wheelbarrow-safety.html

## Slide 20: Best Practices
Lifting
  Firmly grip handles and lift with the knees, not the back
Speed
  Do not move too quickly because, when heavily loaded, a wheelbarrow can have significant momentum and it is hard to stop abruptly
  Keep moving forward instead of starting and stopping
http://www.google.com/images
Source: http://www.ehow.com/about_6396476_wheelbarrow-safety.html

## Slide 21: Best Practices
Obstacles
  Define a clear pathway
  Look ahead to avoid obstacles by going around them
  Go over any obstacles at a right angle to avoid tipping the wheelbarrow
http://www.google.com/images
Source: http://www.ehow.com/about_6396476_wheelbarrow-safety.html

## Slide 22: Best Practices
Inclines
  Avoid inclines if possible
    going up, the wheelbarrow can roll back down and run over the worker. It is important to have adequate momentum so the wheelbarrow can be pushed all the way to the top of the incline without stopping
    going down, the wheelbarrow can pick up speed and get out of control
http://www.google.com/images
Source: http://www.ehow.com/about_6396476_wheelbarrow-safety.html

## Slide 23: Think Safety Work Safely